Height control unit for all high-precision plasma cutting applications. The KHC4-PCS system provides all the essential functions that are needed for consumable-saving piercing and a constant height control as a condition for good cut quality.

- For all HiFocus and FineFocus applications

- Installation or retrofit to any guiding system possible for modernisation of existing cutting workstations

- Integrated 3-dimensional collision protection

- Working load up to 12 kg

- Lifting 220 mm

Features

- Easy adaption to all common guiding systems,

- Tactile finding of initial position on work-piece surface (smooth touching), pressure for initial position finding is adjustable and thus also possible for thin sheets.

- Height adjustment in 0.1 millimeter steps („cutting height mode“) or in 0.5 Volt steps („arc voltage mode“).

- High work-piece utilisation due to precise height measurement also close to kerfs and edges. (On kerfs, edges and corners the arc lengthens and the arc voltage increases. The automatic kerf detection switches the height control off when the arc voltage exceeds the adjustable limit. It is again activated when the voltage value is back to the origninal level. The guiding system transfers a signal as soon as a corner is cut (corner function). In this case, too, the arc is prevented from being too long and having a negative influence on the cut quality.)

- Additionally adjustable height increase during piercing protects the consumables from spatter (slag),

- Adjustment of short torch lifting between contours possible

- Torch clamp with 3D collision protection with +/-17 ° deflection, optionally with intelligent collision detection,

- Adjustable weight compensation

- High lifting speed of max. 80 mm/s,

- Controls for dynamic at linear drive (control response time and control delay time)

- Standard connection with CUTBUS® for 
CNC control via guiding system or alternatively 
with Operator Terminal

- Isolated arc voltage input from 0 to -300 VDC

Display and Control Unit

- Manual adjustment via Operator Terminal

- KCU 4 is the interface between height control unit, 
plasma cutting unit and CNC-control of the guiding system

Technical Data

|  | KHC4-PCS (Linear Drive with Kjellberg Connection Unit KCU 4 and Operator Terminal) |
| --- | --- |
| Working load | Up to 12 kg |
| Lifting | 220 mm standard, 350 mm (option) |
| Max. lifting speed | 80 mm/s |
| Torch clamp for torch diameter | 30-58 mm |
| Collision protection for torch | Deflection ca. ±17° in all directions Collision protection (automatic torch lifting) Automatic resetting Deflection force adjustable |
| Operating voltage | 230 V AC/ 110V AC Auto Select Input |
| Isolated input for arc voltage | 0 to -300 V DC or 0 to 10V |
| Piercing time | 0.2 – 5 s |
| Weight | 9 kg (Linear Drive) 0.4 kg (Operator Terminal) |
| Dimensions | Linear Drive 400 x 125 x 128 mm (H x W x D) (without guide bar) Operator Terminal 120 x 160 x 35 mm (H x W x D) |

# Text boxes

Linear Drive with plasma torch

Kjellberg Connection Unit KCU 4 and Operator Terminal