- Compact system with 1000 Watt Fiber Laser source for cutting and marking of mild steel, stainless steel and aluminum

- For the cutting of thin plates with all common CNC cutting machines, suitable for plasma cutting, (standard plasma cutting tables and more dynamic systems)

- To be used as a single application or alternately with a plasma cutting machine in the same guiding system

- Integrated technology database with wide range of cutting speeds

- Superb surface quality with low roughness

- Taper free and dross free surfaces without time-consuming after-treatment

- Precise cutting of small contours; narrow kerfs

- Very high repeatability and dimensions accuracy

- Non-contact processing

Plug & Play

Complete solution with all components including process control and entire cutting data base for the integration into cutting systems. All components are matched.

- 1 kW fiber laser with processing fiber 20 m

- Active cooling unit integrated

- Control unit with technology database (LC)

- Automatic gas supply (LGV)

- Laser cutting head connection unit (LBA)

- Height control unit (KHC 4 LAS)

- Laser cutting head

- Complete cable and hose package

Technology Database

- Contains complete cutting process incl. hole and edge cutting regime and thereby all required parameter (laser, gas, height control, laser cutting head, automatic focus positioning) for laser cutting

- Up to 9 various cutting speeds based on materials its thicknesses, depending on contour size and dynamic of the guiding system

- Operator select only optimized cutting parameter for the guiding system and contour on basis of material, material thickness, gas and cutting speed

Laser Cutting Head

- Automatic focus positioning

- Displaying of contamination of protection glass

- Cutting and marking with the same consumables

Gas Control

- Automatic laser gas console LGV

- Automatic regulation of gas pressure based on material and its thickness

Technical Data

| Laser source | XFocus 1000 |
| --- | --- |
| Power Connection | 400-480 V; 3 Ph; 50/60 Hz |
| Connected load | 7 kVA (100 % d. c.) |
| Fuse, slow | GL / GG 32 A oder 32 A „C“ |
| Power cable: | 4 x 6 mm² Cu |
| Protection class | IP 22 |
| Temperature | 5 – 40°C |
| “Cold start”-temperature | 20°C |
| Cutting range (mild steel) Maximum Recommended | 10 mm 0,5 - 6 mm |
| Cutting range (stainless steel) Maximum Recommended | 5 mm 0,3 – 4 mm |
| Cutting range (Aluminium) | 1 - 3 mm |
| Fiber laser |  |
| Rated output power | 1000 W |
| Wavelength | 1070 nm (± 5 nm) |
| Modulation rate | 5 kHz |
| Duty cycle pulsing | 100 µs |
| Pilot laser | < 1,0 mW |
| Fiber | Fiber diameter 100 µm |
| Laser protection class | Class 4 (DIN EN 60825-1) |
| Chiller | Compressor chilling |
| Coolant | Deionized Water |
| Conductivity | < 15 µS/cm |
| Pressure | max. 5 bar |
| Flow rates | Laser source circuit min. 8 l/min, Laser head circuit min. 2 l/min |
| Coolant temperature range | 21 - 25 °C |
| Cooling capacity | 3 kW |
| Dimensions (L x W x H) | 1035 x 695 x 1590 mm |
| Weight | 300 kg |

| Laser Cutting Head |  |
| --- | --- |
| Cutting gas connection | G ¼”, max. 25 bar |
| Gases | O2 (10 bar), N2 (20 bar), Air (20 bar) |
| Water chilling | max. 5 bar, flow rate min. 2 l/min |
| Weight | ca. 6 kg |

Notice: All mentioned cutting and piercing thicknesses depend on material, cutting technology and guiding system.