| • Compact system with 2000 Watt Fiber Laser source for cutting and marking of mild steel, stainless steel and aluminum • For the cutting of thin plates with all common CNC cutting machines, suitable for plasma cutting, (standard plasma cutting tables and more dynamic systems) • To be used as a single application or alternately with a plasma cutting machine in the same guiding system • Integrated technology database with wide range of cutting speeds • Superb surface quality with low roughness • Taper free and dross free surfaces without time-consuming after-treatment • Precise cutting of small contours; narrow kerfs • Very high repeatability and dimensions accuracy • Non-contact processing |  |
| --- | --- |

Plug & Play

Complete solution with all components including process control and entire cutting data base for the integration into cutting systems. All components are matched.

- 2 kW fiber laser with processing fiber 20 m

- External cooling unit

- Control unit with technology database (LC)

- Automatic gas supply (LGV)

- Laser cutting head connection unit (LBA)

- Height control unit (KHC 4 LAS)

- Laser cutting head

- Complete cable and hose package

Technology Database

- Contains complete cutting process incl. hole and edge cutting regime and thereby all required parameter (laser, gas, height control, laser cutting head, automatic focus positioning) for laser cutting

- Up to 9 various cutting speeds based on materials its thicknesses, depending on contour size and dynamic of the guiding system

- Operator select only optimized cutting parameter for the guiding system and contour on basis of material, material thickness, gas and cutting speed

Laser Cutting Head

- Automatic focus positioning

- Displaying of contamination of protection glass

- Cutting and marking with the same consumables

Gas Control

- Automatic laser gas console LGV

- Automatic regulation of gas pressure based on material and its thickness

Technical Data

| Laser source | XFocus 2000 |
| --- | --- |
| Power Connection | 400/3P + PE @ 50 Hz or 460/3P + PE @ 60 Hz |
| Connected load | 7 kVA (100 % ED) |
| Temperature | 5 - 40°C |
| air humidity | 10 – 95 % |
| Storage temperature | -40 – 75°C (without water) |
| Cutting range (mild steel) Maximum Recommended | 15 mm 0.5 - 10 mm |
| Cutting range (stainless steel) Maximum Recommended | 8 mm 0.3 – 6 mm |
| Cutting range (Aluminium) Maximum Recommended | 6 mm 0.3 – 4 mm |
| Fiber laser |  |
| Rated output power | 2000 W |
| Wavelength | 1070 nm (± 10 nm) |
| Modulation rate | 5 kHz |
| Duty cycle pulsing | < 1,0 mW |
| Pilot laser | Fiber diameter 100 µm |
| Dimensions (L x W x H) | 1250 x 810 x 1500 mm |
| Weight | 300 kg |
| Laser protection class | Class 4 (DIN EN 60825-1) |

| Chiller |  |
| --- | --- |
| Power connection | 400/3P + PE @ 50 Hz or 460/3P + PE @ 60 Hz |
| Connected load | 15 kVA |
| Number of cooling circuits | 2 |
| Design point | 33°C |
| Air volume | 5600 m³/h |
| Temperature | 10 - 40°C |
| Storage temperature | -40 – 64°C (without water) |
| Coolant | Deionized Water |
| Pressure | max. 2 bar |
| Flow rates | Laser source circuit min. 30 l/min, Laser head circuit min. 2 l/min |
| Coolant temperature | Laser 21°C (± 1K), head 25°C(± 1K) |
| Cooling capacity | 17 kW |
| Dimensions (L x W x H) | 630 x 815 x 1660 mm |
| Weight | 400 kg (without water) |

| Laser Cutting Head |  |
| --- | --- |
| Cutting gas connection | G ¼”, max. 25 bar |
| Gases | O2 (10 bar), N2 (20 bar), Air (20 bar) |
| Water chilling | max. 5 bar, flow rate min. 2 l/min |
| Weight | ca. 6 kg |

Notice: All mentioned cutting and piercing thicknesses depend on material, cutting technology and guiding system.